## Slide 1: Down the Drain
Brad Rafferty
14 June 2020
Image Processing Analysis on a Sink Vortex Flow

## Slide 2: Contents
  Experimental Setup
  Raw Data
  Analysis Methods
  Results
  Summary and Future Work

## Slide 3: Experimental Setup
Camera, Lighting, Action

## Slide 4: Experimental Setup
  Sink drain with garbage disposal
  Water seeded with mica powder
  Lighting overhead and away from drain center
  Record top-down video with cellphone at 30 frames per second
  Process:
    Prime flow by swirling it
    Remove drain plug
    Engage garbage disposal for 1-2 seconds
    Disengage disposal, allow to drain
  Analysis will track properties of the vortex core
phone
Fig 1. Experimental setup, water unseeded
Fig 2. Experimental setup, water seeded with mica powder

## Slide 5: Raw Data
Example Raw Videos

## Slide 6: Raw Videos
  Originally recorded just clear water
    Many features in the flow, however very difficult to detect and quantify repeatably and reliably
  Utilized Mica to help isolate the core, allow options for velocity analysis
    Darker core contrasts against the lighter surface flow, enabling detection readily
    Prevents background noise, e.g. from the sink drain label
  Video capture at 30 fps, 1920x1080
    Wide field-of-view captured, then cropped in processing
Vid 1. Sink vortex flow, water unseeded
Vid 2. Sink vortex flow, water seeded with mica powder

## Slide 7: Analysis Methods
Image Processing & Feature Detection

## Slide 8: Image Processing
  Reference image of sink drain used to determine lengthscale (from diameter) and the center of the frame (center of drain)
  Steps:
    Trim, crop, and center video
    RGB to gray
    Enhance contrast
    Complement (gray high signal)
    Binarize (global threshold, Otsu’s method)
  Note: execute image processing on large field of view of the flow, then crop to region of interest within the binarized frames for feature detection
    This achieves a higher signal-to-noise ratio with the core most distinguishable compared to image processing on a small region of interest from the start
Vid 3. Raw Video
Vid 4. Grayscale, enhanced, complement
Vid 5. Binarized

## Slide 9: Feature Detection
  To isolate the core in binary image:
    bwareafilt() to remove all features but the largest one (assumed to be core)
    bwconncomp() to retrieve the connected component object
    regionprops() to retrieve various data on the conn. Comp:
      Centroid, area, perimeter, etc.
      Convert from px to cm using scaling factor (drain diameter)
    bwboundaries() to extract boundaries of core, for visualization
  Calculate distance of core centroid from origin (drain center)
Vid 6. Grayscale video with detected core centroid (red) and perimeter (green) overlaid

## Slide 10: Results

## Slide 11: Results for One Realization, 1 of 2
  The vortex core grows rapidly before reaching a maximum area
    The area goes to a local minimum before increasing again as it approaches the drain
  Circularity is noisy (due to the rippling edge of the core), and decreases as the core approaches the drain
  The distance of the core to the center of the drain decreases, on average, over time
    The distance has an interesting sinusoidal nature
Fig 3. Core area over time
Fig 4. Core circularity over time
Fig 5. Core diameter over time
Fig 6. Core distance to sink center

## Slide 12: Results for One Realization, 2 of 2
  The core centroid is most likely to dwell in a location that corresponds to a negative x and negative y
    i.e., the centroid favors to hover over a certain sector of the drain
Fig 7. 2D chaos plot of core centroid location for one realization
Fig 8. 3D chaos plot of core centroid location over time for one realization

## Slide 13: Results for Multiple Realizations, 1 of 2
  To maintain a meaningful definition of time: = time after first maximum in core area
  The results repeat quite well, namely:
    The magnitude of core areas falls within a set range
    The trends of circularity, area, etc. over are very similar
Fig 10. Core circularity over time
Fig 9. Core area over time
Fig 11. Core diameter over time
Fig 12. Core distance to sink center

## Slide 14: Results for Multiple Realizations, 2 of 2
  The core centroid has a larger offset in the -direction compared to the -direction
    See histogram over all runs
  The experiment data appear to be non-deterministic and stationary
Fig 13. Probability density function of core centroid location with respect to the sink center, in x- and y-dimensions

## Slide 15: Summary
Takeaways &
Future work

## Slide 16: Summary and Future Work
  Summary
    Sink vortex flow is rich with features and plenty of opportunity for analysis
    Order of operations in image processing requires thoughtful consideration
    Repeatable experimental setup (lighting, camera location) can dictate data quality
  Future Work
    Point detectors on unseeded flow
    PIV analysis (circulation, compare flow to point vortex + sink flow superposition)
Fig 14. Particle image velocimetry analysis on one image pair of the vortex flow
Fig 15. Velocity vectors derived from PIV on one pair of images